## Slide 1: Lecture 3 Negative Feedback
vo = A(v+ - v-)
v+
v-
Open Loop: A ~ 105 almost never used

## Slide 2: NEGATIVE feedback is BETTER than POSITIVE feedback
Consider a Heater control System:
When the temperature falls, the heater turns on
When the temperature rises, the heater turns off
Let vin represent input from a thermometer
v0 represent the control signal to the heater: v0 high → heater on
v0
vin
When it’s cold, vin falls → vo falls → v- decreases → (v+ - v-) increases
→ vo = A(v+ - v-) will tend to rise i.e. heater turns on.
NEGATIVE feedback: something happens→ the system tries counteract it

## Slide 3: Simple Negative feedback
Consider a Heater control System:
When the temperature falls, the heater turns on
When the temperature rises, the heater turns off
v0
vin
vo = A(v+ - v-)
vo = A(vin - vo)
vo (1+A) = A vin
A large
In steady state, v0 tracks vin

## Slide 4: Negative feedback makes inputs equal
v+ and v- are equal – how and why ?
v0
vin
vo = A(v+ - v-)
Output does whatever it can to make the inputs equal

## Slide 5: Golden Rules of Negative Feedback
Output does whatever it can to make inputs equal v- is ‘slave’ to v+ in negative feedback
Inputs draw no current

## Slide 6: Summary
Today:
Negative feedback
Golden Rules I and II of negative feedback