## Slide 1: Lecture 4 Analysis of Negative Feedback
Reference:
1. The mathematics glossed over in this presentation can be found in the online textbook “Opamps for everyone” by Texas Instruments:
http://www.ti.com/lit/ml/sloa077/sloa077.pdf http://www.ti.com/lit/an/sloa049b/sloa049b.pdf
2. Other standard textbooks on electronics like “Introduction to Analog and Digital Electronics” by Agarwal and Lang (several copies in IIT-B central library)

## Slide 2: R2/R1 important – what factors to consider when choosing Ri ?
R2 small → vo needs to source large current: subtracts from the current available to load.
R2 large → parasitic capacitances in combination with large R
introduce non-linear elements into the loop
What is large R?
What is small R?
As a thumb rule, O(10kΩ) is OK. O(1Ω) is small. O(1MΩ) is large.

## Slide 3: Loop gain changes with frequency
0.01
0.1
1
10
102
103
104
105
106
frequency (Hz)→
Gain G →
102
103
104
105
106
frequency (Hz)→
Phase difference Δφ (degrees) →
0◦
-45◦
-90◦
BODE plot
Unity gain at 106 Hz
Δφ at unity gain = -115◦

## Slide 4: Bode plot summarizes the feedback loop characteristics
Gain (dB)
log(f)
AOL
20 dB/decade
AOL=1
Gain Bandwidth Product (GBWP) ≡ frequency at which gain = 1 : property of the device
Units = Hz
“Useable” range as an open loop amplifier
For LM741, AOL = 120 dB, GBWP ~ 106 Hz
→ at 20 dB/decade OL Gain starts dropping already at 1 Hz!
For LM741 = 106 = 20 log10(106) = 120 dB

## Slide 5: With feedback – we increase the frequency range of operation
Gain (dB)
log(f)
AOL
40 dB/decade
G=1
“Useable” frequency range of amplifier has increased by decreasing gain to G=10
employing negative feedback
G=10

## Slide 6: When does negative feedback (good) go bad (positive)?
Generic negative Feedback loop
vout = A ∙ a = A ∙ (vin – Bvout)
If phase shift is 180◦ or more here, the ‘-’ sign effectively becomes ‘+’ : negative feedback will become positive! → amplifier will oscillate with no vin (just noise)
B can be a reactive/active circuit → puts phase shift in the term Bvout

## Slide 7: How do you predict phase of negative feedback ?
Gain (dB)
log(f)
AOL
20 dB/decade
G=1
Gain (dB)
log(f)
AOL
40 dB/decade
G=1
G=10
Phase Δφ
log(f)
0◦
Each pole introduces -90◦ of Δφ
G=1
“dominant pole”
-90◦
Phase Δφ
log(f)
0◦
Δφ < -90◦
G=1
< -90◦

## Slide 8: When is an opamp ‘unity gain stable’?
Gain (dB)
log(f)
AOL
20 dB/decade
G=1
Phase Δφ
log(f)
0◦
Each pole introduces -90◦ of Δφ
G=1
“dominant pole”
Δφ = -90◦
Phase Δφ
log(f)
0◦
phase margin:
180◦ - Δφ when G = 1
Gain (dB)
log(f)
AOL
40 dB/decade
G=1
Dominant pole
pole 2
20 dB/decade
Δφ = -90◦
LM741 is Unity Gain Stable

## Slide 9: How to choose an opamp?
Design inputs:
What is the desired bandwidth? B
What is the desired gain? G
Requirements:
Choose an opamp with a GBWP of at least G∙B
b) Look at the phase response of the chosen opamp in the data sheet, especially at high frequencies near B –
Is the phase margin sufficient? Phase margin ≡(180◦ - Δφ) at G=1, should be at least 45◦ in good design.
c) Why is (b) necessary?
Answer: You can control the design, but not vin !
For example stray noise can be of very high frequency, where the amplifier’s phase shift may be > 180◦
If so, your circuit will oscillate.

## Slide 10: Summary
Today:
Analysis of negative feedback
Phase response, and why it matters
  phase shift in feedback loop > 180◦ can turn negative feedback into positive
How to choose an opamp for a specific application

## Slide 11: Reactive feedback is used in active filters
http://www.analog.com/library/analogdialogue/archives/43-09/active_filters.pdf
vin
vout
R
C
Passive low-pass
has G < 1
introduces phase
vin
vout
Lab 4
Active low-pass
Can set G ≥ 1
introduces phase