## Slide 1: Lecture 5 Opamp imperfections
Reference:
Analog Devices, Opamp basics tutorial:
http://www.analog.com/static/imported-files/tutorials/MT-038.pdf

## Slide 2: Consider opamp internals
OpAmp integrates precision matched actives+passives in one IC
Input Stage
Output Stage
Intermediate gain stages

## Slide 3: Simplified input stage
IE
Ibias+
Ibias-
IERC

## Slide 4: Imperfection 1: Vos
IE
Ibias+
Ibias-
Input offset voltage Vos
IE+RC
IE-RC
IE+
IE –
If IE + and IE – are different, voltages at the collector terminals will be different

## Slide 5: You can compensate Vos
Input Stage
Adjust IE+ & IE-

## Slide 6: Imperfection 2: Ibias
Ibias+
Ibias-
Ibias+≠ Ibias-
Sets the two transistors at two different Q points

## Slide 7: Cannot compensate for Ibias
Ibias+
Ibias-
Good news: Ibias is usually very very small

## Slide 8: Ibias can be bad in a poor circuit
Ibias+
Ibias-
Bad news: Ibias multiplies Rin
Depending on Rin,will cause a fake Ibias+Rin appear as v+ even if vin=0

## Slide 9: Must ‘bias compensate’ a circuit
1. At DC, with Vin = 0, what is the effective R ‘looking out’ from - ?
2. If there is Ibias-, what is effective Vin ?
3. If Ibias+ ≈ Ibias- what must you do at the + terminal to cancel (2)

## Slide 10: Must have equal DC resistance ‘looking’ out of each input terminal
1. Calculate effective R ‘looking’ out from ‘-’ terminal
3. Reff*Ibias+ voltage drop cancels Reff* Ibias- at Vin = 0
2. Put in equivalent Reff in the other ‘+’ terminal

## Slide 11: Preparation for Lab 5
Read up on background of Vos & Ibias
Techniques for measuring Vos & Ibias not trivial! - measure an intrinsic property of the device without applying Vin