## Slide 1: Lecture 6 Review of Instrumentation Amp Impedance matching – power transfer
Reference:
“bible” of RF circuit design:
Thomas H. Lee “The design of CMOS Radio-Frequency Integrated Circuits”

## Slide 2: Review of Lab 5 – Instrumentation Amplifier
Impedance looking into V1
Set V2 to zero
→ v+ = 0
→ v- = v+ = 0
→ V1 sees resistance R to ground
Impedance looking into V2
Set V1 to zero
→ No current into v+
→ Can ‘ignore’ the bulk of the circuit
→ V1 sees resistance 2R to ground

## Slide 3: Response of difference amplifier
Difference Response:
V1 ≠ 0, V2 = 0
v- = (Vout – V1)/2 v+=0 → v-=0 → Vout=V1
V2 ≠ 0, V1 = 0
v+ = V2/2; i+ = V2/R; i- = Vout/R i+ + i- = 0 → (Vout + V2)/R = 0 →Vout = - V2
Superposition: Vout = V1 – V2
Common mode response
V1 = V2 = Vcm
v+ = Vcm/2 v- = Vcm/2 (by golden rule)
v- = (Vout + Vcm)/2 (current sum at v- terminal )
Vout = 0
Assuming ideal case 4 R’s equal
In practice:

## Slide 4: It is best to put the gain stage as close to the input signal as possible
1
1
G
V1
V2
Vo
☺ Inputs see high impedance  Difference amplifier gain G no longer has Acm = 0
 S/N is worsened by noise of unity gain buffer
G
G
1
V1
V2
Vo
☺ Inputs see high impedance ☺ Difference amplifier has Acm = 0
 Need precise component matching to get equal G for V1 and V2

## Slide 5: Kill two stones with one bird Reduce component count, Increase CMRR
☺ Inputs see high impedance
V1
V2
Differential Gain is set by R/Rg
(Easy to calculate by superposition)
☺ All resistors equal except Rg
☺ Vo referred to Vref
Common mode: V1 = V2
v- of OA1 and OA2 are equal (two red dots)
→ No current flows through Rg
☺ Acm~0 within tolerance of 6 R, Rg
V1 → V1’ and V2 →V2’
V1’
V2’