## Slide 1: Lecture 8 Review of Co-axial cable impedance
Reference:
“bible” of RF circuit design:
Thomas H. Lee “The design of CMOS Radio-Frequency Integrated Circuits”
What is “Radio Frequency” ?
Any signal with frequency content 20 kHz to ~ 100 GHz

## Slide 2: A coaxial cable is modelled as a series LC network
See http://goo.gl/l3p7s7 for a detailed analysis of a how a cable ‘works’

## Slide 3: Laboratory 7 – we studied coaxial cables
Source ZS (VS Is)
Cable Z0 (DUT)
Load ZL
Vs Is VR IR
Device Under Test

## Slide 4: Each device must obey Ohm’s law V=I∙Z
Source ZS (VS Is)
Cable Z0 (DUT)
Load ZL
Vs Is VR IR
Device Under Test
2 terminals
4 terminals
2 terminals

## Slide 5: ZL – two terminal device
Load ZL
Vs Is VR IR
2 terminals

## Slide 6: Z0 :superposition (output terminals)
Cable Z0 (DUT)
4 terminals

## Slide 7: Z0 :superposition (input terminals)
Cable Z0 (DUT)
4 terminals

## Slide 8: Solve to get reflection co-eff Γ

## Slide 9: DC v/s AC power transfer
Source ZS (VS Is)
Cable Z0 (DUT)
Load ZL
Vs Is VR IR
AC source
Fig 1
source
Compare – DC power transfer

## Slide 10: Is AC power transfer better than 0.5?
Source ZS (VS Is)
Cable Z0
Load ZL
Vs Is VR IR
AC source
Actually – NO
Source ZS sees load (ZL “through” the cable Z0 ) = Zeff
Max power transfer when ZS = Zeff
But power lost in cable Zo = I2R → can be significant for ~ km’s of cable
v →V
i → i
V→V
i → i
Transformers are used to step UP V and step down i at source
(Substation) transformers are used at load to step down V and step UP i

## Slide 11: Signal transfer requires more thought
Source ZS (VS Is)
Cable Z0
Load ZL
Vs Is VR IR
AC source
Signal being transmitted in the cable has the general form:
Voltage: e-iβz + Γe+i βz for a harmonic signal. (ignoring the eiωt part)
Forward wave
Reflected wave
Lossless
Lossy (cf. Slide 3) β ~ 1/ω
co-ordinate z
High frequency
signals travel slower

## Slide 12: For a source signal (Vg, I) what is the final signal (V,I) delivered to the load?
V0
V0
Must satisfy boundary conditions at both z=0 and z = -l
At z=0, we have already satisfied : V(z) = V0(e-iβz + Γe+i βz)
At z=-l, we must have : Vin = V0(e+iβl + Γe-i βl)
Lossless:
V0, I0 same across Z0
Phase changes
What is V0?

## Slide 13: Signal transmission depends on all the circuit elements (in a bad way!)
V0
V0
Use KVL to express V0 in terms of Vg , Zg , I
Vg = V(z=-l) + ZgI(z=-l)
Vg = V0(e+iβl + Γe-i βl) + Zg V0/Z0 (e+iβl – Γe-i βl )

## Slide 14: Signal transmission depends on l (complex) ZL, Z0
V0
V0
Vg = V0(e+iβl + Γe-i βl) + Zg V0/Z0 (e+iβl – Γe-i βl )
Solve to get:
f(ZL,Z0)!

## Slide 15: Signal transmission depends on l & (complex) ZL, Z0
V0
V0
Even for an ideal lossless cable: Voltage (and hence current) delivered to load depends on l, ZL, Z0