## Slide 1
EP215 Electronics Lab 1
Lecture 3
Review of Lab 2
Simplest Active device: DIODE

## Slide 2
Review of Lab 2
1. One Diode (voltage) clamp
2. Two Diode (voltage) limiter
3. One Diode half-wave rectifier
4. Four diode full-wave rectifier
Fig 1
Vin
Vout
D1
0V
Fig 2
Vin
Vout
D1
D2
Fig 3
Fig 4
D1
D2
D3
D4
OUT
1
2
3
4
Vout
Vin

## Slide 3
What happens in a diode clamp?
Fig 1
Vin
Vout
D1
0V
If Vin < 0.7V, Vout = Vin
If Vin > 0.7V, Vout = 0.7V
Vin
Vout
0.7V
Follow up questions:
1. This circuit only clamps the positive part of Vin What modification would cause it to clamp the negative part of Vin?
2. What modification would make it clamp both positive and negative ?

## Slide 4
What happens in a diode clamp?
Fig 1
Vin
Vout
D1
0V
If Vin > 0.7V, Vout = Vin
If Vin < 0.7V, Vout = 0.7V
Vin
Vout
0.7V
What modification would cause it to clamp the negative part of Vin?

## Slide 5
Diode Limiter
http://www.falstad.com/circuit/e-diodelimit.html
http://www.falstad.com/circuit/e-rectify.html
Half wave Rectifier

## Slide 6
Full wave rectifier
http://www.falstad.com/circuit/e-fullrect.html
D1
D2
D3
D4
OUT
1
2
3
4
Vout
Vin
DSO-1
DSO-2

## Slide 7
Full wave rectifier
with measurements of Vin Vout
http://www.falstad.com/circuit/e-fullrect.html
D1
D2
D3
OUT
1
2
3
4
Vout
Vin
DSO-1
DSO-2

## Slide 8
Full wave rectifier
Looks like a negative clamp from Vin
http://www.falstad.com/circuit/e-fullrect.html
D1
D2
D3
OUT
1
2
3
4
Vout
Vin
DSO-1
Vin
0.7V

## Slide 9
Full wave rectifier
Looks like a half-wave rectifier from Vout
http://www.falstad.com/circuit/e-fullrect.html
D1
D2
D3
OUT
1
2
3
4
Vout
Vin
Vout
DSO-2
Note: D1 and D3 function as positive clamps (like Slide 4)
– but are irrelevant, because the half-wave rectification makes sure that Vout is always positive.

## Slide 10
Full wave rectifier
Looks like a half-wave rectifier from Vout
http://www.falstad.com/circuit/e-fullrect.html
D1
D2
D3
OUT
1
2
3
4
Vout
Vin
Vout
DSO-2
Notice the green dots which represent 0V

## Slide 11
Prep for Lab 3
We have used ‘working’ definitions of Diode operation:
Cathode to Anode voltage > 0.7V → ‘ON’
Cathode to Anode voltage < 0.7V → ‘OFF’
This is not good enough for detailed circuit building & analysis
Vout
0.7V

## Slide 12
I-V characteristics of two terminal devices
As the voltage across a diode increases from 0.65V to 0.75V it changes smoothly from: (V)
A state of not conducting current (I)
To a state of conducting current
We will learn how to determine the I-V characteristics of
any two terminal device without using graph paper!

## Slide 13
Useful reference for this course
http://www.allaboutcircuits.com
“Foundations of Analog and Digital Electronics”
by Anant Agarwal and Jeffrey Lang