## Slide 1: EP315 Microprocessors for Physicists
Physics Experiment
Control
Readout

## Slide 2
Simple control
Room is Hot
AC
Decrease temp setting
Decrease temp setting
Room is cool
AC
Feedback control
comfortable
Stop AC

## Slide 3
Room
Desired Setting = R ◦C
AC
Measure Y ◦C
PROPORTIONAL
Control
Inject cool air
∝ (R – Y)
INTEGRAL
Control
Inject cool air
∝ ∫(R – Y)dt
DERIVATIVE
Control
Inject cool air
∝ d(R – Y)/dt
P
I
D

## Slide 4
Room
Desired Setting = R ◦C
AC
Measure Y ◦C
PID controller applies correction u(t) based on past (integral), present (proportional) & future (derivative)
… or more useful in practice →
Time constants – these are
determined by the time lag in response τdelay of the plant to a step function input in open loop mode. Ratios Τi/ τdelay and Τd/ τdelay
Are determined by Zeigler-Nichols tuning.

## Slide 5
Domestic control example with PID feedback:
Set and maintain the water level in a tank

## Slide 6
References:
http://dexautomation.com/ps/ : flash simulation of PID
… and many others
Accompanying notes on Zeigler Nichols tuning of PID control loop parameters “PracticalTechniquesForPIDTuning”
Lab 03 – PID controller implementation!