## Slide 1
Lecture 3
Finite State Machines
Definition:
A system which has a finite number of states that can be encoded in binary form
The system remembers what state it is in – called the Present State (PS)
Transitions between the states are governed by (usually) deterministic rules – These rules operate upon the input and the PS and cause the FSM to transition to the Next State (NS). At the following time step, the NS becomes the PS.

## Slide 2
The ATmega168 microcontroller,
… or any other microprocessor
functions as a (complex)
Finite State Machine
Details are different depending on the processor architecture:
Number of states
Sequence of state transitions
Delay between transitions (CPU clock)

## Slide 3
ATMega168
Micro-controller
(mostly)
complete diag.

## Slide 5
Arduino Board Design

## Slide 6
There are other,
Simpler
Finite State Machines
we can study in more detail

## Slide 7
Example: Odd Parity Checker
Input: String of 0101001011010….
Objective:
Assert output 1 whenever input bit stream has odd number of 1's
State
Diagram
Three things matter:
Present State i.e. system needs to ‘remember’ its state
Input
Next State
Output is indicated by
Using binary logic, need memory elements:
2 states – 1 bit binary
3 states – 2 bit binary
4 states – 2 bit binary …

## Slide 8
Basic 1-bit memory element:
D register
D
CLOCK
D
CLEAR
Q

## Slide 9
Symbolic State Transition Table
Encoded State Transition Table
Implementation 1 of parity checker:
Next State is calculated based on Input and Present State
Output is equal to the present state of the system
Present State
Even
Even
Odd
Odd
Input
0
1
0
1
Next State
Even
Odd
Odd
Even
Output
0
0
1
1
State
Diagram
Use the FSM State Table to deduce the Boolean Logic function of
Next State= f (Present State, Input)

## Slide 10
Combinational Logic: NS = PS XOR Input
Implementation 1: Output = PS
D
R
Q
Q
Input
CLK
PS=Output
NS
Reset

## Slide 11
Symbolic State Transition Table
Encoded State Transition Table
Implementation 2 of parity checker :
Next State is calculated based on Input and Present State
Output is equal to the next state of the system
Present State
Even
Even
Odd
Odd
Input
0
1
0
1
Next State
Even
Odd
Odd
Even
Output
0
1
1
0
State
Diagram
Output
0
1
1
0
Next State
0
1
1
0
Input
0
1
0
1
Present State
0
0
1
1
Use the FSM State Table to deduce the Boolean Logic function of
Next State= f (Present State, Input)
(Mealy FSM)

## Slide 12
Combinational Logic: NS = PS XOR Input
Timing Behavior: Input 1 0 0 1 1 0 1 0 1 1 1 0
Implementation 2: Output = (PS xor I) = NS
D
R
Q
Q
Input
CLK
PS
Reset
NS=Output
Implementation 1: Output = PS
D
R
Q
Q
Input
CLK
PS=Output
NS
Reset

## Slide 13
1. Moore Machine
Outputs are function of the present state
Outputs change
synchronously with
state changes
2. Mealy Machine
Outputs depend on state AND inputs
Input change causes an immediate output change
Asynchronous outputs
Clock
state
feedback
Combinational
Logic for
Next State
State Register
Outputs
Zk
X
Inputs
i
State Register
Clock
State
Feedback
Combinational
Logic for
Outputs and
Next State
X
Inputs
i
Z
Outputs
k
Present State
Present State
Remember: CLK must enter the Memory element
used to store states of the system!

## Slide 14
Moore-Mealy difference

## Slide 15
Moore-Mealy trade-offs
But… Mealy FSM responds immediately (asynchronously) to Input – Susceptible to Input Glitches in a complex FSM. CLK (which synchronizes change of state) may get delayed in propagating change of state through the memory registers.