## Slide 1
Lecture 4:
Interrupts

## Slide 3
The microprocessor works as a finite state machine.
Instructions are loaded serially from the FlashRAM
Decoded in the instruction decoder
Appropriate sub-functions called as per the instruction (eg: write value to I/O register, perform calculation etc)
These state transitions are orchestrated by the system CPU clock.
With no possibility of ‘indeterminate’ states
loop() function runs continuously

## Slide 4
Sometimes, an input signal may need urgent out-of-turn servicing
i.e. the FSM transition sequence needs to be interrupted
INTERRUPT

## Slide 5
How to service asynchronous signals on the Arduino
As a bare minimum, the Arduino accepts interrupts on digital pins 2 and 3
These are called interrupts 0 and 1
However, the Arduino can be triggered by interrupts
on any of the I/O pins.
A little bit of low-level code needed to set
Interrupt Control Registers..
see Arduino language reference, datasheet,
Look for PCMSK1, PCMSK2, PCICR… and experiment!

## Slide 6
Basic interrupt example
#include <avr/interrupt.h> // must have this to use interrupts
volatile int GlobalSharedVariable = 0;
// this var will be shared by ISR
void setup()
{
attachInterrupt(0, myISR, CHANGE);
// call function myISR every time digital pin 2
// changes state (can also use HIGH or LOW as args)
}
void loop()
{
// twiddle thumbs do other things
// Note: must not change GlobalSharedVariable here!
}
void myISR()
{
GlobalSharedVariable++; // yay! Pin 2 changed state,
// Return to main prog quickly
}

## Slide 7
Stopwatch (Timer) interrupts
Arduino has three special internal ‘Timer’ interrupts
- these work like software stopwatches
Load the timer with a number and start it off.
Every time it counts down to zero, an interrupt is issued
See http://www.arduino.cc/playground/Code/Timer1

## Slide 8
Example:
Interrupts are useful for keeping count of signals that arrive asynchronously.
Objective: Keep track of number of pulses arriving on pin 2
- setup ISR to trigger on HIGH edge detected at pin 2
- ISR increments a variable count
Note: Alternative is to keep ‘polling’ the state of pin 2
using analogRead(2); What is the problem with that?
1) Limited by loop() speed: what if two edges arrive very quickly?
2) What if you want to count number of pulses on pins 1 and 2 at the same time?

## Slide 9
Example:
Want to measure the average
Frequency of pulses on pin 2
Load Timer0 with a number and start it off.
Every time it counts down to zero, an interrupt is issued
- When Timer0 triggers, number of counts on pin 2 is the frequency of waveform on pin 2
(In parallel) have a second ISR running that keeps
count of number of pulses on pin 2
Set Timer0 to run for a period of 1 sec